## Slide 1: QYC Tech Talk
Spring gas and diesel engine maintenance, systems approach

## Slide 2
Essential Maintenance - Bring
Calder’s book
Manual from OPUS V
Spring De-winterize issues of 48 deg North
QUARTERMASTER YACHT CLUB – Essential Maintenance

## Slide 3
QUARTERMASTER YACHT CLUB – Tech Talk Introduction
WELCOME to QYC Tech Talks!
A Tech Talk is…
  An exchange of information, ideas and experience
  More discussion than “teaching”
  A little structure
We encourage…
  Listening, learning & contributing
  Discussion and debate
  Questions
Our next Tech Talk is:
  Weather Apps, May 23, Vashon Library
Together, to Learn From Each Other

## Slide 4
Essential Maintenance
De-winterizing
Boat
Engine
Electric
Hull
Bilge & Through-Hull
Crew Safety
Maintenance Spreadsheet
QUARTERMASTER YACHT CLUB – Essential Maintenance

## Slide 5: De-winterizing Your Boat Wash and clean outside and inside of your boat Check the battery system, including house battery/starter battery, water level and charge and cables for corrosion Test the navigation electronics including VHF Radio, hand held, and fixed, Chart Plotters, Radar, AIS Check and change the engine oil.and filters Check heat exchangers and engine cooling system and inspect raw water inlets, hoses, replace raw water impeller, outboard, inboard, outdrive, replace impellers Inspect the gas tank and fuel lines and replace inline filters, drain fuel water separators Inspect bilges, overall engine inspection, belts, hoses, electrical connections Inspect safety equipment, fire extinguishers, life jackets, make sure handheld VHF batteries are replaced and flares are current

## Slide 6: Essential Boat Maintenance Weekly inspections should be done, focused on making sure equipment is operational. Be sure to check:
Bilge pumps Navigation lights Steering controls | Fuel, water and oil levels, propane VHF radio, test at dock channel 28 Take a look around to identify any hazards

## Slide 7: Essential Boat Maintenance Monthly maintenance begins with cleaning the boat inside and out, checking for general wear and tear. Always inspect:
Engine including bilges, belts, hoses and electrical connections and all motorized equipment Engine oil levels and filters Ropes and lines Safety equipment including life jackets, fire extinguishers, inflatable, and make sure flares haven’t expired House battery and starter battery, check water level, charge cables for corrosion Propellor blades | Navigation electronics including VHF radio, handheld and fixed, chart plotters, radar, and AIS (turn radar on) All electrical items including windscreen wipers and engine tilt Heat exchangers and engine cooling system including inspecting raw water inlets and hoses, and replacing raw water impeller Gas tank and fuel lines, including replacing inline filters and draining fuel water separators

## Slide 8: Essential Boat Maintenance Annual maintenance should include:
Service motor, at least annually or more often depending on how frequently you use your boat Inspect exterior and interior of your vessel looking for cracks, chips, blistering, loose wiring, broken fittings and any other problems Check that grab rails and other fittings are secure and watertight Inspect bottom paint Refresh water systems, holding tanks | Thoroughly inspect the bilge Check steering to ensure controls are running smoothly Clean props, rudders and through hull fittings thoroughly If you cannot fix what you see be sure to raise the issue with your service yard while getting the boat serviced

## Slide 9: Engine Maintenance Engine and fuel system after heavy usage such as a single, long trip Check coolant and oil levels, and top up if necessary Check for, follow up and address any fluid leaks Check oil pads and replace as necessary If you have reached 100 hours of usage (or as per manufacturer’s instructions), replace the oil and filter

## Slide 10: Engine Maintenance Monthly Routine As per manufacturer’s guidance, apply WD40 to engine, components and control panel to prevent corrosion If the boat has not been used that month, start the engine and allow it to reach operating temperature Clean the raw water strainer

## Slide 11: Engine Maintenance Annual Checks Check engine belts for wear and tension. Replace as necessary Check/replace the fuel tank for rust and/or contamination, drain fuel water filters/ separators Ensure the hoses are not cracked and provide enough slack to account for vibration Thoroughly inspect the tank, hose and fittings for evidence of leaks Prior to winter storage, check antifreeze level and replace as necessary. Fill the tank prior to storage as per manufacturer’s instructions Replace spark plugs,, rotor, dist caps, check coil wires, air filters.

## Slide 12: Electric Maintenance After heavy usage Test all batteries for capacity level. Replace if necessary Check that all wiring remains neatly bundled and secured and is well-clear of the exhaust system and bilge

## Slide 13: Electric Maintenance Monthly Maintenance Check all running and interior lights and replace bulbs where required Inspect bulkhead and engine connections to ensure adequate flex with no fraying Check that wire connections and terminals remained sealed, with no corrosion Inspect the hull for evidence of corrosion such as leaks, blistered or peeling paintwork, deposits around stainless steel fixtures or whitish powder on an aluminium hull Inspect all props, shafts, bearings, through-hulls and rudder fittings for corrosion Check steering cables, engine cables and connections and gear casings for corrosion

## Slide 14: Electric Maintenance Annual checks Check water level of battery Clean exterior bulb contact points and apply anti-corrosion spray Replace zincs (either annually or every six months as per manufacturer’s instructions)

## Slide 15: Hull Maintenance Monthly routine Inspect for hull, keel and rudder damage and arrange for any necessary repairs immediately and treat any scratches or gelcoat damage as per manufacturer’s instructions Check the condition of the teak, oil, refinish as necessary

## Slide 16: Hull Maintenance Annual checks All boats require an “annual” haul-out for anti-fouling, zinc replacement (and repainting, where necessary). Contact your maintenance yard well in advance of your preferred haul-out time (usually winter) in order to arrange

## Slide 17: Bilge & Through-Hull Maintenance Monthly routine Even where using automatic pumps, inspect bilges frequently to ensure they are clean and free to circulate Check through-hull strainers, intake and discharge components to ensure they are not blocked by debris or marine growth Ensure valve handles are securely attached to enable quick and smooth closure in an emergency Inspect plugs and hoses for cracking

## Slide 18: Ensuring Crew Safety Pre-departure checks should include checking the presence and placement of all personal flotation devices, first aid kit and flares. Monthly check should include: Thoroughly inspect flotation devices for wear or abrasion. If inflation devices are incorporated into a PFD, ensure cartridges are secure and charged. Check the use-by date on flares Ensure fire extinguishers are in their designated accessible positions, and that they’ve been professionally inspected and appropriately tagged as up to date Ensure lifelines or rails are in good condition Test to ensure CO and fire alarms are working Ensure you are up to date with galley stove inspection and servicing

## Slide 19
QUARTERMASTER YACHT CLUB
Our Next Tech Talk
Location: Vashon Library
Date: Thursday, May 23

## Slide 20
QUARTERMASTER YACHT CLUB – Essential Maintenance
QUESTIONS ?